## Slide 1: Longitudinal registration of standardized MR images (OAI)
Yin Guo
Sep 22, 2020

## Slide 2: Proposed workflow of OAI longitudinal registration
Preprocessing (spatial + intensity standardization)
Segmentation of bone (femur) at baseline
Rigid registration of femur at later time points
Refine registration of vessel (popliteal artery) at later time points
An extended application: segmentation of cartilage
Validation

## Slide 3: 1. Preprocessing
Spatial standardization
  Read dicom images and save headers
  Change orientation to RAI (right, anterior, inferior)
  Change laterality if knee side is right
  Set origin to zero
Intensity standardization
  Rescale intensity to [0,100]
  Potentially: Correct intensity nonuniformity[1],
  edge preserving smoothing[2]…
[1] Sled IEEE TMI 1998
[2] Shan Med Image Anal 2014

## Slide 4: 2. Segmentation of bone (femur) at baseline
Active contours, atlas-based, graph-based, machine and deep learning, and hybrid combinations…
Here, segmentation by registration
Reference image: from pyKNEEr demo
Registration framework: elastix & transformix
Bonaretti PLoS One 2020
Femur mask
Cartilage mask
50% fm blend
50% cm blend

## Slide 5: Segmentation by registration
Step 1 Register moving to reference image
  In our case, moving: baseline scan (L&R) of each OAI subject
  rigid + similarity + spline
  Registration mask: r fm (15 pixels dilated)
reference (pyKNEEr)
9404954L
baseline
9404954R
baseline
50% r fm blend
50% r fm blend

## Slide 6: Segmentation by registration
Step 1 Register moving to reference image
Step 2 Invert transformation
  In our case, i_spline +i_similarity + i_rigid
  How to compute an inverse transformation?
  In elastix, setting initial transform as the transform to be inverted
  Optimization metric: Displacement magnitude penalty

## Slide 7: Segmentation by registration
Step 1 Register moving to reference image
Step 2 Invert transformation
Step 3 Warp reference mask to moving mask
  Level set rather than binary mask: reduce aliasing artifacts
9404954L
baseline
50% warped r fm blend
9404954R
baseline
50% warped fm blend
Whitaker IEEE VVGS 2000
Notes: Inverted transformations are applied to the mask of the reference image to obtain the mask of the moving image. This filter implements a surface-fitting method for estimation of a surface from a binary volume. This process can be used to reduce aliasing artifacts which result in visualization of binary partitioned surfaces.

## Slide 8: 3. Rigid registration of femur at later time points
Registration mask: baseline femur (segmented in 2, 15 pixels dilated)
9404954L 50% r fm blend
12mo
24mo
48mo
72mo
96mo
reference
(baseline)

## Slide 9: How about the vessel?
9404954L 50% r vm blend
baseline
12mo
24mo
48mo
72mo
96mo
How to quantify?
Dice score (intersection over union)
FRAPPE baseline vessel mask v.s. transformed (rigid) TPx vessel mask
96mo

## Slide 10: 4. Refine registration of vessel at later time points
Method 1 do nothing
  Also transform FRAPPE centerlines and vessel wall contours
Method 2 non-rigid transform of the vessel
  Initial transform: rigid (transformed in 3)
  Registration mask: baseline vessel (from FRAPPE, 15 pixels dilated)
baseline
12mo
24mo
48mo
72mo
96mo
9404954L
50% r vm blend

## Slide 11
12mo
24mo
48mo
72mo
96mo
baseline

## Slide 12: Also, segment by registration!!!
With method 2 (vessel registration refinement), inversely, we can directly segment outer wall contours at later time points!!!
Step 1 Register moving to reference image
  Femur rigid + vessel spline
Step 2 Invert transformation
  i_spline + i_rigid
Step 3 Warp reference mask to moving mask
  Baseline ➡️ TPx vessel mask
Dice score: segmented TPx vessel map v.s. FRAPPE TPx vessel map

## Slide 13: 5. An extended application: cartilage segmentation
Segmentation by registration

## Slide 14: Validation
5 cases, L&R, all time points available ➡️ 58 instances
4 instances totally fail (at rigid, excluded)
Dice score 1 (FRAPPE baseline vessel mask v.s. transformed (rigid) TPx vessel mask): 0.673
Dice score 2 (segmented TPx vessel map v.s. FRAPPE TPx vessel map, 0.816
9911265R 96mo

## Slide 15: Future thoughts
Does register femur rigidly suffice?
What about tibia?
Does non-rigid vessel registration tamper vessel feature?
If not, how to validate?